## Slide 1: The Plural Architecture Shared Memory Many-core with Hardware Scheduling
Ran Ginosar
Technion, Israel
Oct 2017
and

## Slide 2: Outline
Motivation: Programming model
Plural architecture
Plural implementation
Plural programming model
Validation
Plural programming examples
ManyFlow for the Plural architecture

## Slide 3: many-cores
Many-core is:
  a single chip
  with many (how many?) cores and on-chip memory
  running one (parallel) program at a time, solving one problem
  an accelerator
Many-core is NOT:
  Not a “normal” multi-core
  Not running an OS
Contending many-core architectures
  Shared memory (the Plural architecture, XMT)
  Tiled (Tilera, Godson-T)
  Clustered (Rigel)
  GPU (Nvidia)
Contending programming models

## Slide 4: Why manycores? Scaling
We know of VLSI scaling
  Going forward with technology
  See VLSI course
Another scaling: More cores using same technology
  Example: Start with one core
    Voltage V1
    Frequency ≈ performance = f1
    Power P1 ≈ C V12
  Move to 2 cores
    Voltage V2 = 0.8 V1
    Frequency f2 = 0.8 f1
    Performance = 2 f2 = 1.6 f1
    Power P2 = 2C V22 =2C (0.8 V1)2 = 2×0.64 C V12 = 1.3 P1
  Conclusions
    Increasing frequency is dead
    Naïve parallelism is naïve
    Manycore scaling can scale

## Slide 5: Context
Plural:
  homogeneous acceleration
  for heterogeneous systems
HOST
OS
I/O
Network
Peripherals
Plural Accelerator
streaming

## Slide 6: One (parallel) program ?
Best formal approach to parallel programming is the PRAM model
Manages
  all cores as a single shared resource
  all memory as a single shared resource
and more…
Joseph F. JaJa, Introduction to Parallel Algorithms, 1992
Cormen, Leiserson, Rivest, Stein,
Introduction to algorithms,
2009

## Slide 7: PRAM matrix-vector multiply
×
=
The PRAM algorithm
is row index
Begin
  yi=Aix
End
A,x,y in shared memory
(Concurrent Read of x)
Temp are in private memories (e.g. computing actual addresses given )
Ax=y
Ai
x
yi
×
=
×
=
×
=
×
=
×
=
Core 0
Core 1
Core 2
Core 3
Core 4

## Slide 8: PRAM logarithmic sum
The PRAM algorithm
// Sum vector A(*)
Begin
  B(i) := A(i)
  For h=1:log(n)
  if then
  B(i) = B(2i-1) + B(2i)
End
// B(1) holds the sum
a1
a2
a3
a4
a5
a6
a7
a8
h=3
h=2
h=1
B(i)=A(i)
if (..) B(i)=B(2i-1)+B(2i)
h
h
(fine grain) tasks
many
identical tasks

## Slide 9: Advantages of PRAM-like programming
Simpler program
  Flat memory model
  Same data structures as in serial code
  No code for finding and moving the data
  Easier programming, lower energy, higher performance
  Scalable to higher number of cores

## Slide 10: Advantages of PRAM-like programming
Same-node Scalability
  Easy to define high levels of parallelism
  Scalable to more cores running slower at lower voltage
    on same technology node
  Example: same-node-scaling from N to 2N cores same-node-scaling of Vdd and f by = 0.8, … ,0.5
 | N cores, Vdd, f | 2N cores, Vdd, f | = 0.8 | = 0.7 | = 0.6 | = 0.5
Perf |  |  |  |  |  | 
Time |  |  |  |  |  | 
Power |  |  |  |  |  | 
Energy |  |  |  |  |  | 
Perf / Pwr |  |  |  |  |  | 
 | N cores, Vdd, f |  |  |  |  | 
Perf |  |  |  |  |  | 
Time |  |  |  |  |  | 
Power |  |  |  |  |  | 
Energy |  |  |  |  |  | 
Perf / Pwr |  |  |  |  |  | 

## Slide 11: Outline
Motivation: Programming model
Plural architecture
Plural implementation
Plural programming model
Validation
Plural programming examples
ManyFlow for the Plural architecture

## Slide 12: The Plural Architecture: Part I
“Anti-local” address interleaving Negligible conflicts
Many small processor cores Small private memories (stack, L1 caches)
P
P
P
P
P
P
P
P
Off-chip memory, IO
Shared Memory
P-to-M resolving NoC
Fast NOC to memory (Multistage Interconnection Network) NOC resolves conflicts
SHARED memory, many banks ~Equi-distant from cores (2-3 cycles)

## Slide 13: The Plural Architecture: Part II
P
P
P
P
P
P
P
P
P-to-M resolving NoC
Low (zero) latency parallel scheduling enables fine granularity
scheduler
P-to-S scheduling NoC
Hardware scheduler / dispatcher / synchronizer
Shared Memory
“Anti-local” address interleaving Negligible conflicts
Many small processor cores Small private memories (stack, L1)
Fast NOC to memory (Multistage Interconnection Network) NOC resolves conflicts
SHARED memory, many banks ~Equi-distant from cores (2-3 cycles)
external memory, IO

## Slide 14: Outline
Motivation: Programming model
Plural architecture
Plural implementation
Plural programming model
Validation
Plural programming examples
ManyFlow for the Plural architecture

## Slide 15: How does the P-to-M NOC look like?
Full bi-partite connectivity required
But full cross-bar not required: minimize conflicts and allow stalls/re-starts
P
P
P
P
P
P
P
P
P
P
P
P
M
M
M
M
M
M
M
M
M
M
M
M

## Slide 16: Logarithmic multistage interconnection network
P
P
P
P
P
P
P
P
P
P
P
P
M
M
M
M
M
M
M
M
M
M
M
M
Pipeline stage (registers)
Combinational switches

## Slide 17: Floor plan and route to shared memory

## Slide 18: access sequence: fixed latency (when successful)
time
Processors
MEMORY
pipeline stage 3
Pipeline Stage 1
Pipeline Stage 2
cycle
Read Request
NACK
NACK
NACK

## Slide 19: Floor plan: 64 DSP cores (24KB each) & 4MB shared memory take 320 mm2 on 65nm
20.4 mm
15.5 mm
(32+16) × 0.8 Gb/s
12 × 2 × 6.25 Gb/s

## Slide 20: RC64

## Slide 21: Outline
Motivation: Programming model
Plural architecture
Plural implementation
Plural programming model
Validation
Plural programming examples
ManyFlow for the Plural architecture

## Slide 22: Three levels of “parallel” programming
Multiple Plural chips
  Distributed computing (message passing)
  OR: shared memory
The Plural chip
  64 cores, shared memory
A high performance DSP core
  VLIW + SIMD
P
P
P
P
P
P
P
P
P-to-M resolving NoC
scheduler
P-to-S scheduling NoC
Shared memory

## Slide 23: The Plural task-oriented programming model
Programmer generates TWO parts:
  Task-dependency-graph
  Sequential task codes
Task graph loaded into scheduler
Tasks loaded into memory
regular
duplicable taskName ( instance_id )
{
… instance_id ….
// instance_id is instance number
…..
}
Task template:
P
P
P
P
P
P
P
P
P-to-M resolving NoC
scheduler
P-to-S scheduling NoC
Shared memory

## Slide 24: Fine Grain Parallelization
Convert (independent) loop iterations
  for ( i=0; i<10000; i++ ) { a[i] = b[i]*c[i]; }
into parallel tasks
  set_task_quota(doLargeLoop, 10000)
  void doLargeLoop(unsigned int id) { a[id] = b[id]*c[id]; } //id is instance number
duplicable doLargeLoop

## Slide 25: Task graph example (2D FFT)
Duplicable task
…
…
…
…
…
…
Condition
Join / fork
Singular task

## Slide 26: Another task graph (linear solver)

## Slide 27: Linear Solver: Simulation snap-shots

## Slide 28: Cores and Tasks
Core
Task
known to scheduler

## Slide 29: Hardware Scheduler: Under the hood
task #
Instance #
…
0
1
2
core #
…
total instances
# already allocated
…
0
1
2
task #
…
state
dependencies
state
task graph

## Slide 30: Plural Task Oriented Programming Model: Task Rules 1
Tasks are sequential
All ready tasks, or any subset, can be executed in parallel on any number of cores
All computing organized in tasks. All code lines belong to tasks
Tasks use shared data in shared memory
  May employ local private memory.
  Its contents disappear once a task completes
Precedence relations among tasks:
  Described in task graph
  Managed by scheduler: receive task completion messages, schedule dependent tasks
Nesting task spawning is easy and natural

## Slide 31: Plural Task Oriented Programming Model: Task Rules 2
2 types of tasks:
  Regular task (Executes once)
  Duplicable task
    Many independent concurrent instances
    Identified/dispatch: entry point, instance number
Conditions on tasks checked by scheduler
Tasks are not functions
  No arguments, no inputs, no outputs
  Share data only in shared memory
No synchronization points other than task completion
  No BSP, no barriers
No locks, no access control in tasks
  Conflicts are designed into the algorithm (they are no surprise)
  Resolved only by P-to-M NoC

## Slide 32: Outline
Motivation: Programming model
Plural architecture
Plural implementation
Plural programming model
Validation
Plural programming examples
ManyFlow for the Plural architecture

## Slide 33: Concurrency in shared memory manycore
Non-preemptive execution
Task graph defines tasks and dependencies
Task graph executed by scheduler
 path ti  tk  ti, tk are non-concurrent
  Execution of ti must complete before start of execution of tk
Otherwise, ti, tk are concurrent May execute simultaneously or at any order
Task graph must be decomposable into concurrent sets
ti
tk
tk
ti

## Slide 34: (verifiable) Shared Memory Access Rules
Predictable Addressing
  Shared memory address derivable at compile time
  No data-dependent shared memory addresses
  Predictable malloc() address
Exclusive Write (EW)
  Task ti writes into A  compiler can verify that no concurrent task tk allowed to access A (neither read nor write)
Concurrent Read (CR)
  Compiler can verify that Concurrent tasks may read from same address but none of them may write into it

## Slide 35: Outline
Motivation: Programming model
Plural architecture
Plural implementation
Plural programming model
Validation
Plural programming examples
ManyFlow for the Plural architecture

## Slide 36: Example: Matrix Multiplication
set_task_quota(mm, N*N); // create N×N tasks
extern float A[],B[],C[] // A,B,C in shared mem
void mm(unsigned int id) // id = instance number
{
i = id mod N; // row number
k = id / N; // column number
sum = 0;
for(m=0; m<N; m++){
sum += A[i][m] * B[m][k]; // read row & column from
// shared mem
}
C[i][k] = sum; // store result in shared mem
}
duplicable MM

## Slide 37: Algorithms and their performance
Matrix multiplication
  RTD by Ramon Chips
Image processing
  RTD by TU Braunschweig, DSI, DLR, ELBIT/ELOP
    Hyperspectral imaging
    SAR imaging
Modem
  RTD by Ramon Chips

## Slide 38: Matrix Multiplication on RC64
Each result element is computed by a task
  For N×N matrices, N×N tasks (regardless of #cores)
Later, each task computes an entire row of
  Only N tasks

## Slide 39: Matrix Multiplication on RC64
#define MSIZE 100
float A[MSIZE][MSIZE], B[MSIZE][MSIZE],
C[MSIZE][MSIZE];
int mm_start() REGULAR
{ int i,j;
for (i=0; i< MSIZE; i++)
for (j=0; j< MSIZE; j++)
{ A[i][j] = 13; B[i][j] = 9; }
}
void mm (unsigned int id) DUPLICABLE
{ int i,j,m; float sum = 0;
i = id % MSIZE; j = id / MSIZE;
for (m=0; m < MSIZE; m++)
sum += A[i][m]*B[m][j];
C[i][j]=sum;
}
int mm_end () REGULAR
{ printf("finished mm\n"); }
#define MSIZE 100
#define MMSIZE 10000
regular mm_start()
duplicable mm(mm_start) MMSIZE
regular mm_end(mm)
CODE (plain C)
TASK GRAPH
duplicable mm
regular mm_start
regular mm_end

## Slide 40: Matrix Multiplication on RC64
Why is SU(1024) still less than 1024?
SPEEDUP & THRUPUT

## Slide 41: Matrix Multiplication using only N tasks
#define MSIZE 100
float A[MSIZE][MSIZE], B[MSIZE][MSIZE],
C[MSIZE][MSIZE];
int mm_start () REGULAR
{ int i,j;
for (i=0; i< MSIZE; i++)
for (j=0; j< MSIZE; j++)
{ A[i][j] = 13; B[i][j] = 9; }
}
void mm_ntasks (unsigned int id) DUP
{ int m, k; float sum = 0;
for (k=0; k<MSIZE; k++) {
sum = 0;
for (m=0; m < MSIZE; m++)
sum += A[id][m]*B[m][k];
C[id][k]=sum;
}
}
int mm_end () REGULAR
{ printf("finished mm with N tasks\n"); }
#define MSIZE 100
regular mm_start()
duplicable mm_ntasks(mm_start) MSIZE
regular mm_end(mm_ntasks)
CODE (plain C)
TASK GRAPH
duplicable mm_ntasks
regular mm_start
regular mm_end

## Slide 42: Matrix Multiplication using only N tasks
What went wrong ?
SPEEDUP & THRUPUT
EFFICIENCY

## Slide 43: DVB-S2x MODEM on RC64
Developed at Ramon Chips
DVB-S2 is critical to modern communication satellites

## Slide 44: DVB-S2 transmit—three stages

## Slide 45: Many-Flow: DVB-S2x Modem
SHARED MEMORY
DMA
DMA
SW on Cores
DMA
LDPC
accelerator
Samples
Data bits
SW
LDPC
SW
IN
OUT
Task graph:
SW on Cores

## Slide 46: Many-Flow: software pipeline
Frame group
k
Frame group
k+1
Frame group
k+2
Frame group
k+3
Frame group
k+4

## Slide 47: DVB-S2x task graph

## Slide 48: Many-Flow: Double buffering
Frame group
k
Frame group
k+1
Frame group
k+2
Frame group
k+3
Frame group
k+4

## Slide 49: Performance of DVB-S2 on RC64
Tx 2.3 Gb/s
Rx 1.0 Gb/s

## Slide 50: SW development flow: MATLAB to RC64
MATLAB float, unrestricted (also SIMULINK)
MATLAB float, restricted memory size and I/O
MATLAB fixed point 16-bit
  Insert DSP library functions
  Create Golden model
Convert to C
  Sequential code on laptop
  Bit-exact comparison to Golden model
Parallelize for RC64 many-core. Create task graph
  Simulate using “many-task emulator” on laptop
  Bit-exact comparison to Golden model
Transfer to RC64
  Execute on hardware, or
  Simulate using cycle-accurate RC64 simulator
  Bit-exact comparison to Golden model

## Slide 51: What if parallelism is limited ?
So far, examples were highly parallel
What if algorithm CANNOT be parallelized?
  Execute many (serial) instances in parallel
  Each instance on different data
What if algorithm is mixture of serial / parallel segments?
  Use ManyFlow

## Slide 52: Outline
Motivation: Programming model
Plural architecture
Plural implementation
Plural programming model
Validation
Plural programming examples
ManyFlow for the Plural architecture

## Slide 53: Stream Processing
Data arrives in a sequence of blocks
In parallel:
  Process current block (K)
  Output results of previous block (K-1)
  Input next block (K+1)
time
Process block K
K + 1
K - 1
Output block K-1
Input block K+1
Output block K
Input block K+2
Output block K-2
Input block K
Process
Out+In
data block cycle time

## Slide 54: PIPELINED stream processing
For faster data & slower processing
time
Process block K
K + 3
Input block K
Process block K+1
K + 4
Process block K+2
K + 5
K - 1
K - 2
K - 3
K - 4
K - 5
Input K-1
Input K-2
Input K+2
Input K+1
Input K+4
Input K+3
Input K+6
Input K+5
Output K-4
Output K-5
Output K-6
Output K-2
Output K-3
Output block K
Output K-1
Output K+2
Output K+1
data block cycle time

## Slide 55: PIPELINED stream processing: ManyFlow
Parallel execution of pipelined stream processing on the shared-memory manycore Plural architectures
Flexible, dynamic, out-of-order, task-oriented execution

## Slide 56: Example: A DWT image compression algorithm
)
A
B
C
)
D
E
56
B
A
C
D
E
Low utilization: only 65%
Image compression time: 160 (relative time units)
DWT
(highly parallel *)
Bit-plane
encoding
(highly parallel *)
Time
Num. cores
utilized
Max 64 cores
serial
serial
serial

## Slide 57: Speed it up with a pipeline?
25
50
18
54
13
=160
54
54
54
54
54
Sequential
Pipeline

## Slide 58: Hardware-like Pipeline
Needs 5 stages: two with 64 cores each, three with one core each (total 131 cores)
If only 64 cores, time / step = 64x2 + 25 = 153 (how ? What is the utilization?)
Hard to program, inefficient, inflexible, fixed task per core. Need to store 5 images
Step i
Time step i+1
Step i+2
Step i+3
Step i+4
Step i+5
Step i+6
Step i+7
Image k+4
Image k+5
Image k+6
Image k+7
Image k+3
Image k+2
Image k+1

## Slide 59: Parallel / pipelined “ManyFlow”
All 5 stages are independent (order does not matter)
Can run concurrently
Scheduler will dispatch most efficiently
)
A
B
C
)
D
E
Pipeline Stage Sync
Image
k
Image
k+1
Image
k+2
Image
k+3
Image
k+4
Step i
Still need to store 5 images (and their temporary storage)

## Slide 60: Parallel / pipelined “ManyFlow”
)
A
B
C
)
D
E
Input
raw image
Output
compressed image
Pipeline Stage Sync
Task graph for continuous execution
Includes two more pipe stages, for I/O of images
Now need to store 7 images (and their temporary storage)

## Slide 61: Parallel / pipelined “ManyFlow” (automatically scheduled)
Higher utilization: 99%
B
A
C
D
E
Image compression time (piped): 95

## Slide 62: The code
PROGRAM
#include <stdio.h>
#include <stdlib.h>
#include <string.h>
#define N 1000
int round_counter = 0;
void program_start() {
set_task_quota(BB,N);
set_task_quota (DD,N);
}
void AA (void) { set_task_runtime(25); }
void BB (void) { set_task_runtime(3); }
void CC (void) { set_task_runtime(20); }
void DD (void) { set_task_runtime(3); }
void EE (void) { set_task_runtime(10); }
int task_manager(void) {
round_counter++;
if (round_counter < 5)
return(0);
else
return(1);
}
void program_end(void) { }
TASK graph
regular task program_start()
regular task AA (program_start || task_manager==0)
regular task CC (program_start || task_manager==0)
regular task EE (program_start || task_manager==0)
duplicable task BB (program_start || task_manager==0)
duplicable task DD (program_start || task_manager==0)
regular task task_manager (AA && BB && CC && DD && EE)
regular task program_end (task_manager==1)
(for simplicity, real task code replaced by indication of duration)

## Slide 63: Challenges
What if on-chip memory is limited?
  Input & output to/from same area
  Process smaller data blocks
  Decompose algorithm to fewer steps
    Beware of combining serial and parallel code segments in same pipe stage
    Stages may be serial, highly parallel, or limited parallel

## Slide 64: Example: JPEG compression algorithm using ManyFlow
RGB pixel stream
Convert RGB
to YCrCb
Compress
color 4:2:0
DCT 8X8
16X16 pl
Y,Cr,Cb
8X8 pl
4Y 1Cr 1Cb
Quantization
8X8 Coeff
4Y 1Cr 1Cb
DPCM
ZigZag Scan
DC
AC
8X8 Coeff
4Y 1Cr 1Cb
DC Huffman
AC Huffman
8X8 Coeff
4Y 1Cr 1Cb
Combine
Bit Stream
DC
AC
DC
AC
Variable Length code
4Y 1Cr 1Cb
Compressed bit stream

## Slide 65: JPEG compression: ManyFlow

## Slide 66
JPEG compression: Task Allocation

## Slide 67
JPEG compression: Most cores active

## Slide 68: Example: JPEG2000 Encoder
Parallel fraction =95%
A
B
C
D
E
Number of busy cores
X10 msec
Serial: 220 msec
Parallel:
1280/64=20 msec
Serial: 60 msec
Parallel:
1920/64 = 30 msec
Serial: 70 msec
Serial time sec
Parallel time msec
Speed-up:
Efficiency:
Image: 8b pixels
Core frequency MHz
A
C
E
B
D

## Slide 69: Non-ManyFlow RIGID Multi-Job Scheduling
Run multiple serial sections in parallel
Run a single parallel section at a time
A
B
C
D
E
A
B
C
D
E
A
B
C
D
E
A
B
C
D
E
A
B
C
D
E
A
B
C
D
E
A
B
C
D
E
A
B
C
D
E
S
T

## Slide 70: Non-ManyFlow RIGID Multi-Job Scheduling
Fixed number of cores p=64
Job with fraction parallel, serial
  Time of parallel section
Variable number of Jobs J=1,2,…
Schedule:
  J serial sections in parallel, time
  J parallel sections in series, time
Serial time
Parallel time
JPEG2000, J=1, =95%
J=16

## Slide 71: Non-ManyFlow RIGID Multi-Job Scheduling
Memory-limited
8MB (¼ max memory) enables:
  J=16 jobs
  Speed-up 50 (cf. 9)
  0.8 efficiency (cf. 0.14)
    ManyFlow works better !
JPEG2000, J=1
J=16

## Slide 72: Advantages of the Plural Architecture
Shared, uniform (~equi-distant) memory
  no worry which core does what
  no advantage to any core because it already holds the data
Many-bank memory + fast P-to-M NoC
  low latency
  no bottleneck accessing shared memory
Fast scheduling of tasks to free cores (many at once)
  enables fine grain data parallelism
Any core can do any task equally well on short notice
  scales well
Programming model:
  intuitive to programmers
  CREW verifiable
  “easy” for automatic parallelizing compiler (?)

## Slide 73: Summary
Simple many-core architecture
  Inspired by PRAM
Hardware scheduling
Task-based programming model
Designed to achieve the goal of ‘more cores, less power’
Developing model to illuminate / investigate