## Slide 1: The Plural Architecture: Simulation using Many-Task Emulator (MTE)

## Slide 2: Simulation on laptop using MTE
Task graph {A, then B || C}
MTE emulator (P=1)
  Issues tasks based on dependencies
  Reconstructs time line
“real” Plural execution
A
B
C
B, tB
C, tC
A, tA
tA
start
end
tB
tC
A, tA
B, tB
C, tC
Many Task Emulator

## Slide 3: MTE (Many-Task Emulator)
Plural Manycore (e.g. RC64) | MTE
e.g. 64 processors | programmable, from 1 to any number
Parallel | Emulated – serial execution
e.g. DSP | X86
Instruction cache (I$) Data cache (D$) Local Memory (LM) | None. May be emulated by user SW
Hardware Scheduler | Emulated – managed by MTE
Shared memory (e.g. 4MB) | Unlimited. May be emulated by user SW
I/O | Emulated
Accelerators | None. May be emulated by user SW
Host control & monitor | None

## Slide 4: Tasks
Regular task
  Sequential, single instance
  Returns 1/0 (true/false) “token” (may be ignored)
Duplicable task
  Sequential, many concurrent instances
  Quota set/changed by program (or set in task.map)
  Instance number available to instance code
Dummy task
  Unallocated, useful for token algebra
File specifying the task graph

## Slide 5: Other tasks
High priority task
  Pre-empts other tasks on a core
  For handling I/O etc.
  On termination, send “software event” interrupt to scheduler

## Slide 6: Task graph segments (in task.map)
OR
AND
OR-AND
OR-AND

## Slide 7: Setting up MTE
Make sure in BIOS that Intel/AMD Virtualization Technology (one or two options! Everything starting with V?) is/are enabled
Install Oracle VM Virtualbox from
  https://www.virtualbox.org/wiki/Downloads
Download (also) the extension (if not offered to do so by installer)
  Virtual Box Manager (VBM) file-->preferences-->extensions (add package button) click on the obvious item, install
After starting the Virtual Box Manager, possibly need to disable Display3D acceleration (on VBM home page)(if you get such a warning during Login)
Get the virtual machine
  4GB file MTE-RC-ubuntu-20161103.OVA from this link (https://technionmail-my.sharepoint.com/personal/ran_technion_ac_il/_layouts/15/guestaccess.aspx?guestaccesstoken=%2bPodu8tTL3%2bey82NJJDqdaW2RuScRtyuP4siMKZIi8g%3d&docid=0705a53c88b064fed81322dbc3ae389d3&rev=1)
Import VM into VB
  VBM file-->import appliance --> select MTE-RC-ubuntu-20161103.OVA, Import
Set up sharing with your Windows host file system (HFS)
  VBM Settings (button)  Shared Folders  Add button (+), select your directory (can repeat many), check Auto-mount
Start VM
  VBM Start (green arrow button)
Login
  User ramon-users
  Password ramon
Start eclipse

## Slide 8: New project in MTE
Eclipse Project Explorer (EPE)
  Right clicknewproject, select wizard C/C++C/C++ project, NEXT
  Enter project name, select Project type: Makefile:Empty project, select Toolchains: Linux GCC, Finish
  Select the new project, right clickImportGeneral:File System, NEXT
  Either:
    Browse to /usr/local/ramon-chips/examples/template_emulator_project (or pulldown)
    Select Makefile, task.map, source/source.c,
    Finish
  Or:
    Browse to a HFS archive
    Select Makefile, task.map[*], source/*.c, *.h
    Finish

## Slide 9: Execute a project
EPE (Eclipse Project Explorer), select project, right click, Close Unrelated Projects
EPE, select project, right click, Clean Project
EPE, select project, right click, Build Project
  Watch Console for errors and warning
Run button (>) or right click, Run As,…
EPE, select project, right click, Refresh (F5)
Peruse
  rc_utilization.csv
  rc64.log

## Slide 10: Simple do-nothing example
source.c
int round_counter = 0;
int A_func (void)
{ set_current_task_time_cycles(10); printf("start parallel\n"); }
void B_func (unsigned int instance) { set_current_task_time_cycles(15); }
void C_func (unsigned int instance) { set_current_task_time_cycles(20); }
void D_func (unsigned int instance) { set_current_task_time_cycles(25); }
void E_func (unsigned int instance) { set_current_task_time_cycles(30); }
int F_func (void)
{ set_current_task_time_cycles(35); printf("end parallel\n"); }
int cnt_func(void) {
set_current_task_time_cycles(5);
round_counter++;
if (round_counter < 4) { return 0; }
else { return 1; }
}
Task graph
dummy d() // 0
regular A(d || cnt==false) //10
duplicable B(A) 2000 //15
duplicable C(B) 2500 //20
duplicable D(A) 2600 //25
duplicable E(C && D) 2300 //30
regular cnt(E) // 5 regular F(cnt==true) // 3
A
B
C
E
cnt
F
D
d
true
false

## Slide 11: Simple: utilization chart
4 rounds
A
B
D
C
E
F

## Slide 12: Changing number of processing cores
A command line argument to MTE
-cores=NUMBER

## Slide 13: Simple: Speedup & Efficiency on 1-1024 cores
Pull down the Run As… menu
Select Run Configurations…
Go to (x)= Arguments tab
Type “ –cores=256” or any p
Rerun, refresh and record the new Tp

## Slide 14: Matrix Multiplication (N2 tasks)
#define MSIZE 100
float A[MSIZE][MSIZE], B[MSIZE][MSIZE], C[MSIZE][MSIZE];
int program_start_func ()
{ read / generate input matrices }
void mm_func(unsigned int id)
{ int i,k,m; float sum = 0;
i = id % MSIZE;
k = id / MSIZE;
for (m=0; m < MSIZE; m++)
sum += A[i][m]*B[m][k];
C[i][k]=sum;
}
int program_end_func()
{ printf("finished mm\n"); }
#define MSIZE 100
#define MMSIZE 10000
regular program_start()
duplicable mm(program_start) MMSIZE
regular program_end(mm)

## Slide 15: Force my own estimated run times
#include <stdlib.h>
#define MSIZE 100
#define MUL_TIME 1
#define ADD_TIME 1
#define LDST_TIME 5
#define DIV_TIME 5
float A[MSIZE][MSIZE], B[MSIZE][MSIZE], C[MSIZE][MSIZE];
int program_start_func ()
{ read / generate input matrices ; set_current_task_time_cycles(10); }
void mm_func(unsigned int id)
{ int i,j,m; float sum = 0; int runTime = 0;
i = id % MSIZE; k = id / MSIZE;
for (m=0; m < MSIZE; m++) {
sum += A[i][m]*B[m][k];
runTime += MUL_TIME*5 + ADD_TIME*3 + LDST_TIME*0 + DIV_TIME*0;
}
C[i][k]=sum;
runTime += MUL_TIME*5 + ADD_TIME*4 + LDST_TIME*1 + DIV_TIME*1;
set_current_task_time_cycles(runTime);
}
Int program_end_func()
{ printf("finished mm\n"); set_current_task_time_cycles(10); }

## Slide 16: Matrix Multiplication: works well
Why is SU(1024) still less than 1024?

## Slide 17: Matrix Multiplication with only N=100 tasks