## Slide 1: The Roofline Model: A pedagogical tool for program analysis and optimization
Samuel Williams1,2, David Patterson1,
Leonid Oliker1,2, John Shalf2, Katherine Yelick1,2
1University of California, Berkeley
2Lawrence Berkeley National Laboratory
samw@cs.berkeley.edu
Notes: Developed not only to easily explain differences in performance among architectures, but also requisite optimizations

## Slide 2: Outline
Motivation, Goals, Audience, etc…
Survey of multicore architectures
Description of the Roofline model
Introduction to Auto-tuning
Application of the roofline to auto-tuned kernels
  Example #1 - SpMV
  Example #2 - LBMHD
Conclusions

## Slide 3: Motivation
Multicore guarantees neither good scalability
nor good (attained) performance
Performance and scalability can be extremely non-intuitive even to computer scientists
Success of the multicore paradigm seems to be premised upon their programmability
To that end, one must understand the limits to both scalability and efficiency.
- How can we empower programmers?
Notes: …. How can we aide them ?

## Slide 4: Primary Focus
Throughput-oriented kernels (rather than time)
Our performance metrics are:
Gflop/s and % of peak (efficiency)
for purposes of this talk, I will focus on memory-intensive
64b floating-point SPMD kernels.
Not focused on algorithmic innovation or
computational complexity

## Slide 5: Goals & Audience
Goals for Roofline:
  Provide everyone (especially undergrads) with a graphical aid that provides: realistic expectations of performance and productivity
  Show inherent hardware limitations for a given kernel
  Show potential benefit and priority of optimizations
Who’s not the audience for the Roofline:
  Not for those interested in fine tuning (+10%)
  Not for those challenged by parallel kernel correctness

## Slide 6: Multicore SMPs of Interest
(used throughout the rest of the talk)

## Slide 7: Multicore SMPs Used
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
HyperTransport
Opteron
Opteron
Opteron
Opteron
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
Opteron
Opteron
Opteron
Opteron
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
2MB Shared quasi-victim (32 way)
SRI / crossbar
2MB Shared quasi-victim (32 way)
SRI / crossbar
HyperTransport
4GB/s
(each direction)
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
8 x 6.4 GB/s
(1 per hub per direction)
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
VMT
PPE
512K
L2
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
VMT
PPE
512K
L2
<20GB/s
(each direction)
AMD Opteron 2356 (Barcelona)
Intel Xeon E5345 (Clovertown)
IBM QS20 Cell Blade
Sun T2+ T5140 (Victoria Falls)
667MHz FBDIMMs
Chipset (4x64b controllers)
10.66 GB/s(write)
21.33 GB/s(read)
10.66 GB/s
Core
FSB
Core
Core
Core
10.66 GB/s
Core
FSB
Core
Core
Core
4MB
shared L2
4MB
shared L2
4MB
shared L2
4MB
shared L2
Notes: NOTE: SMP, NUMA?, Snoop Filter?

## Slide 8: Multicore SMPs Used
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
HyperTransport
Opteron
Opteron
Opteron
Opteron
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
Opteron
Opteron
Opteron
Opteron
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
2MB Shared quasi-victim (32 way)
SRI / crossbar
2MB Shared quasi-victim (32 way)
SRI / crossbar
HyperTransport
4GB/s
(each direction)
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
8 x 6.4 GB/s
(1 per hub per direction)
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
VMT
PPE
512K
L2
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
VMT
PPE
512K
L2
<20GB/s
(each direction)
AMD Opteron 2356 (Barcelona)
Intel Xeon E5345 (Clovertown)
IBM QS20 Cell Blade
Sun T2+ T5140 (Victoria Falls)
667MHz FBDIMMs
Chipset (4x64b controllers)
10.66 GB/s(write)
21.33 GB/s(read)
10.66 GB/s
Core
FSB
Core
Core
Core
10.66 GB/s
Core
FSB
Core
Core
Core
4MB
shared L2
4MB
shared L2
4MB
shared L2
4MB
shared L2
Conventional Cache-based
Memory Hierarchy
Disjoint Local Store
Memory Hierarchy

## Slide 9: Multicore SMPs Used
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
HyperTransport
Opteron
Opteron
Opteron
Opteron
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
Opteron
Opteron
Opteron
Opteron
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
2MB Shared quasi-victim (32 way)
SRI / crossbar
2MB Shared quasi-victim (32 way)
SRI / crossbar
HyperTransport
4GB/s
(each direction)
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
8 x 6.4 GB/s
(1 per hub per direction)
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
VMT
PPE
512K
L2
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
VMT
PPE
512K
L2
<20GB/s
(each direction)
AMD Opteron 2356 (Barcelona)
Intel Xeon E5345 (Clovertown)
IBM QS20 Cell Blade
Sun T2+ T5140 (Victoria Falls)
667MHz FBDIMMs
Chipset (4x64b controllers)
10.66 GB/s(write)
21.33 GB/s(read)
10.66 GB/s
Core
FSB
Core
Core
Core
10.66 GB/s
Core
FSB
Core
Core
Core
4MB
shared L2
4MB
shared L2
4MB
shared L2
4MB
shared L2
multithreaded cores

## Slide 10: Multicore SMPs Used (peak double precision flops)
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
HyperTransport
Opteron
Opteron
Opteron
Opteron
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
Opteron
Opteron
Opteron
Opteron
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
2MB Shared quasi-victim (32 way)
SRI / crossbar
2MB Shared quasi-victim (32 way)
SRI / crossbar
HyperTransport
4GB/s
(each direction)
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
8 x 6.4 GB/s
(1 per hub per direction)
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
VMT
PPE
512K
L2
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
VMT
PPE
512K
L2
<20GB/s
(each direction)
AMD Opteron 2356 (Barcelona)
Intel Xeon E5345 (Clovertown)
IBM QS20 Cell Blade
Sun T2+ T5140 (Victoria Falls)
667MHz FBDIMMs
Chipset (4x64b controllers)
10.66 GB/s(write)
21.33 GB/s(read)
10.66 GB/s
Core
FSB
Core
Core
Core
10.66 GB/s
Core
FSB
Core
Core
Core
4MB
shared L2
4MB
shared L2
4MB
shared L2
4MB
shared L2
75 GFlop/s
74 Gflop/s
29* GFlop/s
19 GFlop/s
*SPEs only

## Slide 11: Multicore SMPs Used (total DRAM bandwidth)
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
HyperTransport
Opteron
Opteron
Opteron
Opteron
667MHz DDR2 DIMMs
10.66 GB/s
2x64b memory controllers
Opteron
Opteron
Opteron
Opteron
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
512KB
victim
2MB Shared quasi-victim (32 way)
SRI / crossbar
2MB Shared quasi-victim (32 way)
SRI / crossbar
HyperTransport
4GB/s
(each direction)
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
667MHz FBDIMMs
21.33 GB/s
10.66 GB/s
4MB Shared L2 (16 way)
(64b interleaved)
4 Coherency Hubs
2x128b controllers
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
MT SPARC
Crossbar
179 GB/s
90 GB/s
8 x 6.4 GB/s
(1 per hub per direction)
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
VMT
PPE
512K
L2
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
BIF
512MB XDR DRAM
25.6 GB/s
EIB (ring network)
XDR memory controllers
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
SPE
256K
MFC
VMT
PPE
512K
L2
<20GB/s
(each direction)
AMD Opteron 2356 (Barcelona)
Intel Xeon E5345 (Clovertown)
IBM QS20 Cell Blade
Sun T2+ T5140 (Victoria Falls)
667MHz FBDIMMs
Chipset (4x64b controllers)
10.66 GB/s(write)
21.33 GB/s(read)
10.66 GB/s
Core
FSB
Core
Core
Core
10.66 GB/s
Core
FSB
Core
Core
Core
4MB
shared L2
4MB
shared L2
4MB
shared L2
4MB
shared L2
21 GB/s (read)
10 GB/s (write)
21 GB/s
51* GB/s
42 GB/s (read)
21 GB/s (write)
*SPEs only

## Slide 12: Roofline models for multicore SMPs
(for memory-intensive double precision floating-point kernels)

## Slide 13: Arithmetic Intensity in HPC
True Arithmetic Intensity (AI) ~ Total Flops / Total DRAM Bytes
  constant with respect to problem size for many problems of interest
  ultimately limited by compulsory traffic
  diminished by conflict or capacity misses.
A r i t h m e t i c I n t e n s i t y
O( N )
O( log(N) )
O( 1 )
SpMV, BLAS1,2
Stencils (PDEs)
Lattice Methods
FFTs
Dense Linear Algebra
(BLAS3)
Particle Methods

## Slide 14: Naïve Roofline Model
Based on Bound and Bottleneck analysis1
Performance is upper bounded by both the peak flop rate,
and the product of streaming bandwidth and the flop:byte ratio
(well understood in the performance oriented communities)
where AI is the actual arithmetic intensity
Assumptions:
  Bandwidth is independent on arithmetic intensity
  Bandwidth is independent of optimization or access pattern
  Computation is independent of optimization
  Complete overlap of either communication or computation
1D. Lazowska, J. Zahorjan, G. Graham, K. Sevcik,
“Quantitative System Performance”
Gflop/s(AI) = min
Peak Gflop/s
AI * StreamBW

## Slide 15: Roofline Model
2
1/8
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/4
1/2
1
2
4
8
16
1
Log scale !
Log scale !

## Slide 16: Naïve Roofline Model
Unrealistically optimistic model
Hand optimized Stream BW benchmark
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
peak DP
8
peak DP
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW

## Slide 17: Naïve Roofline Model
Unrealistically optimistic model
Hand optimized Stream BW benchmark
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
peak DP
8
peak DP
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
This level of performance
is only attainable with
extensive optimizations

## Slide 18: Naïve Roofline Model
Unrealistically optimistic model
Hand optimized Stream BW benchmark
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
peak DP
8
peak DP
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
How sensitive is each
architecture to
removing those optimizations ?

## Slide 19: Better Roofline
Collect StreamBWj with progressively fewer optimizations
Estimate InCoreGFlopsi with progressively fewer optimizations
is the attainable performance with:
memory optimizations1…i - and -
in-core optimizations1..j
These denote a series of ceilings below the roofline
Assumptions:
  Bandwidth is independent on arithmetic intensity
  Complete overlap of either communication or computation
GFlopsi,j(AI) = min
InCoreGFlopsi
AI * StreamBWj
Notes: Performance is a combination of in-core and bandwidth optimizations

## Slide 20: Roofline models (dram bandwidth)
What happens as bandwidth optimizations are stripped out ?
Form a series of bandwidth ceilings below the roofline
Small problems fit in the snoop filter in Clovertown’s MCH
most architectures see NUMA and prefetch variations
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
peak DP
8
peak DP
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
Notes: DEFINE CEILINGS !!

## Slide 21: Roofline models (dram bandwidth)
What happens as bandwidth optimizations are stripped out ?
Form a series of bandwidth ceilings below the roofline
Small problems fit in the snoop filter in Clovertown’s MCH
most architectures see NUMA and prefetch variations
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
peak DP
8
peak DP
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
dataset fits in snoop filter
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW

## Slide 22: Roofline models (dram bandwidth)
What happens as bandwidth optimizations are stripped out ?
Form a series of bandwidth ceilings below the roofline
Small problems fit in the snoop filter in Clovertown’s MCH
most architectures see NUMA and prefetch variations
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
8
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
dataset fits in snoop filter
peak DP
peak DP
w/out SW prefetch
w/out SW prefetch
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
IBM QS20
Cell Blade
hand optimized Stream BW

## Slide 23: Roofline models (dram bandwidth)
What happens as bandwidth optimizations are stripped out ?
Form a series of bandwidth ceilings below the roofline
Small problems fit in the snoop filter in Clovertown’s MCH
most architectures see NUMA and prefetch variations
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
8
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
dataset fits in snoop filter
peak DP
peak DP
peak DP
w/out SW prefetch
w/out SW prefetch
unaligned DMA
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW

## Slide 24: Roofline models (dram bandwidth)
What happens as bandwidth optimizations are stripped out ?
Form a series of bandwidth ceilings below the roofline
Small problems fit in the snoop filter in Clovertown’s MCH
most architectures see NUMA and prefetch variations
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
peak DP
8
peak DP
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
w/out SW prefetch
w/out NUMA
dataset fits in snoop filter
unaligned DMA
w/out NUMA
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW

## Slide 25: Roofline models (dram bandwidth)
What happens as bandwidth optimizations are stripped out ?
Form a series of bandwidth ceilings below the roofline
Small problems fit in the snoop filter in Clovertown’s MCH
most architectures see NUMA and prefetch variations
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
peak DP
8
peak DP
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
w/out SW prefetch
w/out NUMA
dataset fits in snoop filter
unaligned DMA
w/out NUMA
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
hand optimized Stream BW
w/out unit stride
w/out unit stride
w/out unitr stride
Notes: What if we don’t have unit-stride accesses ?

## Slide 26: In-core Performance
Define a similar set of ceilings for in-core performance
In-core performance can be limited by (among other things):
  Not satisfying all forms of in-core parallelism:
    Instruction-level parallelism (multi-issue, pipeline, …)
    Data-level parallelism (SIMD)
    Functional unit parallelism (adders + multipliers + …)
  Non-FP instructions can consume instruction issue bandwidth
    As the FP fraction decrease, how sensitive is attainable performance?
One or the other is usually more difficult to satisfy on a given architecture/kernel
= Architecture’s Achilles’ Heel

## Slide 27: Roofline models (in-core performance = in-core parallelism?)
Covering the breadth of in-core parallelism is the preeminent challenge on most architectures
Form a series of parallelism ceilings below the roofline
On Niagara machines, instruction latencies are easily hidden with 8-way multithreading
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
peak DP
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
w/out SIMD
w/out ILP
mul/add imbalance
dataset fits in snoop filter
w/out FMA
peak DP
w/out SIMD
w/out ILP
w/out NUMA
unaligned DMA
8
peak DP
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)

## Slide 28: Roofline models (in-core performance = instruction mix?)
All machines have a limited instruction issue bandwidth.
non-FP instructions sap instruction issue bandwidth needed by FP instructions
As the FP fraction of the dynamic instruction mix decreases, so might performance.
On Cell, double precision instructions stall subsequent issues for 7 cycles.
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Sun T2+ T5140
(Victoria Falls)
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
peak DP
dataset fits in snoop filter
12% FP
25% FP
peak DP
w/out SW prefetch
w/out NUMA
12% FP
25% FP
peak DP
w/out NUMA
unaligned DMA
12%

## Slide 29: Roofline models (Achilles' Heel)
Its clear that in-core parallelism is more important on the superscalars
Instruction mix is more important on Niagara2
Each architecture has its own Achilles’ Heel when it comes to in-core performance
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
w/out SIMD
w/out ILP
mul/add imbalance
dataset fits in snoop filter
w/out FMA
peak DP
w/out SIMD
w/out ILP
w/out NUMA
unaligned DMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
Sun T2+ T5140
(Victoria Falls)

## Slide 30: Roofline models (ceilings constrain performance)
The ceilings act to constrain performance to a much smaller region
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
w/out SIMD
w/out ILP
mul/add imbalance
dataset fits in snoop filter
w/out FMA
peak DP
w/out SIMD
w/out ILP
w/out NUMA
unaligned DMA
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
1/16
1/16
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
Notes: Ceilings constrain performance

## Slide 31: Roofline models (ceilings constrain performance)
The ceilings act to constrain performance to a much smaller region
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
w/out SIMD
w/out ILP
mul/add imbalance
dataset fits in snoop filter
w/out FMA
peak DP
w/out SIMD
w/out ILP
w/out NUMA
unaligned DMA
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
1/16
1/16
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
Notes: Ceilings constrain performance

## Slide 32: Roofline models (thickness)
The ceilings act to constrain performance to a much smaller region
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
w/out SIMD
w/out ILP
mul/add imbalance
dataset fits in snoop filter
w/out FMA
peak DP
w/out SIMD
w/out ILP
w/out NUMA
unaligned DMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
Sun T2+ T5140
(Victoria Falls)
Thickness of the roofline is
indicative of requisite
compiler or SW complexity
Notes: If I were to give you a roofline model and arithmetic intensity, could you predict performance ?

## Slide 33: Three Categories of Software Optimization

## Slide 34: Optimization Categorization
Maximizing
In-core Performance
Minimizing
Memory Traffic
Maximizing
Memory Bandwidth
Exploit in-core parallelism
(ILP, DLP, etc…)
Good (enough)
floating-point balance
?
unroll &
jam
?
explicit
SIMD
?
reorder
?
eliminate
branches
Exploit NUMA
Hide memory latency
Satisfy Little’s Law
?
memory
affinity
?
SW
prefetch
?
DMA
lists
?
unit-stride
streams
?
TLB
blocking
Eliminate:
Capacity misses
Conflict misses
Compulsory misses
Write allocate behavior
?
cache
blocking
?
array
padding
?
compress
data
?
streaming
stores

## Slide 35: Maximizing Attained in-core Performance
2
1/8
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/4
1/2
1
2
4
8
16
Compilers may not have as much knowledge as the programmer
Express more in-core parallelism and amortize non-FP instructions
Software optimizations:
  Explicit SIMDization
  Loop unrolling
  Unroll and jam
  Reordering
  Predication
Punch through ceilings
1
peak SP
AMD Opteron 2356
(Barcelona)
mul / add imbalance
w/out ILP
peak stream bandwidth
w/out SW prefetching
w/out NUMA optimizations
w/out SIMD
compulsory misses
capacity
conflict

## Slide 36: Maximizing Attained Memory Bandwidth
2
1/8
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/4
1/2
1
2
4
8
16
Compilers won’t give great out-of-the-box bandwidth
Optimizations:
  long unit stride accesses
  NUMA aware allocation and parallelization
  SW prefetching
  Maximize MLP
Punch through bandwidth ceilings
1
peak SP
AMD Opteron 2356
(Barcelona)
mul / add imbalance
w/out ILP
peak stream bandwidth
w/out SW prefetching
w/out NUMA optimizations
w/out SIMD
compulsory misses
capacity
conflict

## Slide 37: Minimizing Total Memory Traffic
2
1/8
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/4
1/2
1
2
4
8
16
Use performance counters to measure flop:byte ratio (AI)
Out-of-the-box code may have an AI ratio much less than the compulsory ratio
Optimizations:
  Array padding: conflict
  Cache blocking: capacity
  Cache bypass: compulsory
Push arithmetic intensity to the compulsory limit
1
peak SP
AMD Opteron 2356
(Barcelona)
mul / add imbalance
w/out ILP
peak stream bandwidth
w/out SW prefetching
w/out NUMA optimizations
w/out SIMD
capacity
conflict
compulsory miss limit

## Slide 38: Optimization Categorization
Maximizing
In-core Performance
Minimizing
Memory Traffic
Maximizing
Memory Bandwidth
Exploit in-core parallelism
(ILP, DLP, etc…)
Good (enough)
floating-point balance
?
unroll &
jam
?
explicit
SIMD
?
reorder
?
eliminate
branches
Exploit NUMA
Hide memory latency
Satisfy Little’s Law
?
memory
affinity
?
SW
prefetch
?
DMA
lists
?
unit-stride
streams
?
TLB
blocking
Eliminate:
Capacity misses
Conflict misses
Compulsory misses
Write allocate behavior
?
cache
blocking
?
array
padding
?
compress
data
?
streaming
stores
Each optimization has
a large parameter space
What are the optimal parameters?
Notes: Note the difference between ‘optimization’ and ‘parameter’

## Slide 39: Introduction to Auto-tuning

## Slide 40: Out-of-the-box Code
Out-of-the-box code has (unintentional) assumptions on:
  cache sizes (>10MB)
  functional unit latencies(~1 cycle)
  etc…
These assumptions may result in poor performance when they exceed the machine characteristics

## Slide 41: What is auto-tuning?
Goal: provide performance portability across the existing breadth and evolution of microprocessors
At the expense of a one time up front productivity cost that’s amortized by the number of machines its used on
Auto-tuning does not invent new optimizations
Auto-tuning automates the exploration of the optimization and parameter space
Two components:
  parameterized code generator (we wrote ours in Perl)
  Auto-tuning exploration benchmark
  (combination of heuristics and exhaustive search)
Can be extended with ISA specific optimizations (e.g. DMA, SIMD)

## Slide 42: Distinguishing the Roofline and Auto-tuning
Roofline specifies what's deficient, but not how to fix it.
Auto-tuning attempts to fix it by searching the parameter space for the existing body of optimization work

## Slide 43: Application of the Roofline Model to sample Kernels
Does the roofline model provide insight into the limitations of architecture, implementation, and algorithm?

## Slide 44: notes
Things to watch for:
  do performance graphs alone provide insight into the limitations of kernel or architecture ?
  does the roofline show the ultimate performance limitations of
  kernel and architecture ?
  does the roofline show which optimizations will be necessary ?
Notes: Kernel details aren’t key to this talk.

## Slide 45: Example #1: Auto-tuning Sparse Matrix-Vector Multiplication (SpMV)
Samuel Williams, Leonid Oliker, Richard Vuduc, John Shalf, Katherine Yelick, James Demmel, "Optimization of Sparse Matrix-Vector Multiplication on Emerging Multicore Platforms", Supercomputing (SC), 2007.

## Slide 46: Sparse Matrix Vector Multiplication
What’s a Sparse Matrix ?
  Most entries are 0.0
  Performance advantage in only storing/operating on the nonzeros
  Requires significant meta data to reconstruct the matrix structure
What’s SpMV ?
  Evaluate y=Ax
  A is a sparse matrix, x & y are dense vectors
Challenges
  Very low arithmetic intensity (often <0.166 flops/byte)
  Difficult to exploit ILP(bad for superscalar),
  Difficult to exploit DLP(bad for SIMD)
(a)
algebra conceptualization
(c)
CSR reference code
for (r=0; r<A.rows; r++) {
double y0 = 0.0;
for (i=A.rowStart[r]; i<A.rowStart[r+1]; i++){
y0 += A.val[i] * x[A.col[i]];
}
y[r] = y0;
}
A
x
y
(b)
CSR data structure
A.val[ ]
A.rowStart[ ]
...
...
A.col[ ]
...

## Slide 47: The Dataset (matrices)
Unlike dense BLAS, performance is dictated by sparsity
Suite of 14 matrices
All bigger than the caches of our SMPs
We’ll also include a median performance number
Dense
Protein
FEM /
Spheres
FEM /
Cantilever
Wind
Tunnel
FEM /
Harbor
QCD
FEM /
Ship
Economics
Epidemiology
FEM /
Accelerator
Circuit
webbase
LP
2K x 2K Dense matrix
stored in sparse format
Well Structured
(sorted by nonzeros/row)
Poorly Structured
hodgepodge
Extreme Aspect Ratio
(linear programming)

## Slide 48: SpMV Performance (simple parallelization)
Out-of-the box SpMV performance on a suite of 14 matrices
Scalability isn’t great
Is this performance good?
Naïve Pthreads
Naïve
Notes: Looking at this,
Could an undergrad tell me why scalability is poor?
Could an undergrad tell me how much further improvement is possible?

## Slide 49: Auto-tuned SpMV Performance (architecture specific optimizations)
Fully auto-tuned SpMV performance across the suite of matrices
Included SPE/local store optimized version
Why do some optimizations work better on some architectures?
Performance is better,
but is performance good?
+Cache/LS/TLB Blocking
+Matrix Compression
+SW Prefetching
+NUMA/Affinity
Naïve Pthreads
Naïve

## Slide 50: Auto-tuned SpMV Performance (architecture specific optimizations)
Fully auto-tuned SpMV performance across the suite of matrices
Included SPE/local store optimized version
Why do some optimizations work better on some architectures?
Performance is better,
but is performance good?
+Cache/LS/TLB Blocking
+Matrix Compression
+SW Prefetching
+NUMA/Affinity
Naïve Pthreads
Naïve
Auto-tuning resulted
in better performance,
but did it result in
good performance?

## Slide 51: Roofline model for SpMV
Double precision roofline models
FMA is inherent in SpMV (place at bottom)
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
w/out SIMD
peak DP
w/out ILP
w/out FMA
w/out NUMA
unaligned DMA
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
dataset dataset fits in snoop filter

## Slide 52: Roofline model for SpMV (overlay arithmetic intensity)
Two unit stride streams
Inherent FMA
No ILP
No DLP
FP is 12-25%
Naïve compulsory flop:byte < 0.166
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
w/out SIMD
peak DP
w/out ILP
w/out FMA
w/out NUMA
unaligned DMA
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
No naïve Cell
implementation
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
dataset dataset fits in snoop filter

## Slide 53: Roofline model for SpMV (out-of-the-box parallel)
Two unit stride streams
Inherent FMA
No ILP
No DLP
FP is 12-25%
Naïve compulsory flop:byte < 0.166
For simplicity: dense matrix in sparse format
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
w/out SIMD
peak DP
w/out ILP
w/out FMA
w/out NUMA
unaligned DMA
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
No naïve Cell
implementation
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
dataset dataset fits in snoop filter

## Slide 54: Roofline model for SpMV (NUMA & SW prefetch)
compulsory flop:byte ~ 0.166
utilize all memory channels
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
w/out SIMD
peak DP
w/out ILP
w/out FMA
w/out NUMA
unaligned DMA
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
No naïve Cell
implementation
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
dataset dataset fits in snoop filter

## Slide 55: Roofline model for SpMV (matrix compression)
Inherent FMA
Register blocking improves ILP, DLP, flop:byte ratio, and FP% of instructions
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
w/out SIMD
peak DP
w/out ILP
w/out FMA
w/out NUMA
unaligned DMA
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
dataset dataset fits in snoop filter
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)

## Slide 56: Roofline model for SpMV (matrix compression)
Inherent FMA
Register blocking improves ILP, DLP, flop:byte ratio, and FP% of instructions
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
w/out SIMD
peak DP
w/out ILP
w/out FMA
w/out NUMA
unaligned DMA
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
dataset fits in snoop filter
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
All machines are on the
bandwidth roofline !

## Slide 57: Example #2: Auto-tuning Lattice-Boltzmann Magneto-Hydrodynamics (LBMHD)
Samuel Williams, Jonathan Carter, Leonid Oliker, John Shalf, Katherine Yelick, "Lattice Boltzmann Simulation Optimization on Leading Multicore Platforms", International Parallel & Distributed Processing Symposium (IPDPS), 2008.
Best Paper, Application Track

## Slide 58: LBMHD
Plasma turbulence simulation via Lattice Boltzmann Method
Two distributions:
  momentum distribution (27 scalar components)
  magnetic distribution (15 vector components)
Three macroscopic quantities:
  Density
  Momentum (vector)
  Magnetic Field (vector)
Arithmetic Intensity:
  Must read 73 doubles, and update 79 doubles per lattice update (1216 bytes)
  Requires about 1300 floating point operations per lattice update
  Just over 1.0 flops/byte (ideal)
Out-of-the-box,
no unit stride memory
access patterns
momentum distribution
14
4
13
16
5
8
9
21
12
+Y
2
25
1
3
24
23
22
26
0
18
6
17
19
7
10
11
20
15
+Z
+X
magnetic distribution
14
13
16
21
12
25
24
23
22
26
18
17
19
20
15
+Y
+Z
+X
macroscopic variables
+Y
+Z
+X

## Slide 59: Initial LBMHD Performance
Generally, scalability looks good
but is performance good?
*collision() only
Naïve+NUMA
Notes: PPE performance is abysmal

## Slide 60: Auto-tuned LBMHD Performance (architecture specific optimizations)
Auto-tuning avoids cache conflict and TLB capacity misses
Additionally, it exploits SIMD where the compiler doesn’t
Include a SPE/Local Store optimized version
*collision() only
+Explicit SIMDization
+SW Prefetching
+Unrolling
+Vectorization
+Padding
Naïve+NUMA
+small pages

## Slide 61: Roofline model for LBMHD
Far more adds than multiplies (imbalance)
Huge data sets
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
w/out FMA
peak DP
w/out ILP
w/out SIMD
w/out NUMA
unaligned DMA
peak DP
mul/add imbalance
dataset fits in snoop filter
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
w/out SIMD
w/out ILP

## Slide 62: Roofline model for LBMHD (overlay arithmetic intensity)
Far more adds than multiplies (imbalance)
Essentially random access to memory
Flop:byte ratio ~0.7
NUMA allocation/access
Little ILP
No DLP
High conflict misses
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
w/out FMA
peak DP
w/out ILP
w/out SIMD
w/out NUMA
unaligned DMA
peak DP
mul/add imbalance
dataset fits in snoop filter
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
No naïve Cell
implementation
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Intel Xeon E5345
(Clovertown)
Sun T2+ T5140
(Victoria Falls)
w/out SIMD
w/out ILP

## Slide 63: Roofline model for LBMHD (out-of-the-box parallel performance)
Far more adds than multiplies (imbalance)
Essentially random access to memory
Flop:byte ratio ~0.7
NUMA allocation/access
Little ILP
No DLP
High conflict misses
Peak VF performance with 64 threads (out of 128) - high conflict misses
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
w/out FMA
peak DP
w/out ILP
w/out SIMD
w/out NUMA
unaligned DMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
No naïve Cell
implementation
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Sun T2+ T5140
(Victoria Falls)
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
mul/add imbalance
dataset fits in snoop filter
Intel Xeon E5345
(Clovertown)
w/out SIMD
w/out ILP

## Slide 64: Roofline model for LBMHD (Padding, Vectorization, Unrolling, Reordering, …)
Vectorize the code to eliminate TLB capacity misses
Ensures unit stride access (bottom bandwidth ceiling)
Tune for optimal VL
Clovertown pinned to lower BW ceiling
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
w/out FMA
peak DP
w/out ILP
w/out SIMD
w/out NUMA
unaligned DMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
No naïve Cell
implementation
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Sun T2+ T5140
(Victoria Falls)
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
mul/add imbalance
dataset fits in snoop filter
Intel Xeon E5345
(Clovertown)
w/out SIMD
w/out ILP

## Slide 65: Roofline model for LBMHD (SIMDization + cache bypass)
Make SIMDization explicit
Technically, this swaps ILP and SIMD ceilings
Use cache bypass instruction: movntpd
Increases flop:byte ratio to ~1.0 on x86/Cell
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
w/out FMA
peak DP
w/out ILP
w/out SIMD
w/out NUMA
unaligned DMA
peak DP
w/out ILP
w/out SIMD
mul/add imbalance
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Sun T2+ T5140
(Victoria Falls)
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
mul/add imbalance
dataset fits in snoop filter
Intel Xeon E5345
(Clovertown)
w/out ILP
w/out SIMD

## Slide 66: Roofline model for LBMHD (SIMDization + cache bypass)
Make SIMDization explicit
Technically, this swaps ILP and SIMD ceilings
Use cache bypass instruction: movntpd
Increases flop:byte ratio to ~1.0 on x86/Cell
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
25% FP
peak DP
12% FP
w/out SW prefetch
w/out NUMA
w/out FMA
peak DP
w/out ILP
w/out SIMD
w/out NUMA
unaligned DMA
peak DP
w/out SIMD
w/out ILP
mul/add imbalance
w/out SW prefetch
w/out NUMA
IBM QS20
Cell Blade
Opteron 2356
(Barcelona)
Sun T2+ T5140
(Victoria Falls)
1
2
1/16
flop:DRAM byte ratio
attainable Gflop/s
4
8
16
32
64
128
1/8
1/4
1/2
1
2
4
8
peak DP
mul/add imbalance
dataset fits in snoop filter
Intel Xeon E5345
(Clovertown)
w/out SIMD
w/out ILP
3 out of 4 machines
hit the Roofline

## Slide 67: Conclusions

## Slide 68: Summary
The Roofline model is a visually intuitive figure for kernel analysis and optimization
We believe undergraduates will find it useful in assessing performance and scalability limitations
It is easily extended to other architectural paradigms
We believe it is easily extendable to other metrics:
  performance (sort, graphics, crypto…)
  bandwidth (L2, PCIe, …)
We believe that a performance counters could be used to generate a runtime-specific roofline that would greatly aide the optimization

## Slide 69: Suggestion…
As architectures are presented over the next two days, we invite you to create a roofline model for each.
Estimate the ceilings.
Then contemplate performance and productivity among them

## Slide 70: Acknowledgements
Research supported by:
  Microsoft and Intel funding (Award #20080469)
  DOE Office of Science under contract number DE-AC02-05CH11231
  NSF contract CNS-0325873
  Sun Microsystems - Niagara2 / Victoria Falls machines
  AMD - access to Quad-core Opteron (barcelona) access
  Forschungszentrum Jülich - access to QS20 Cell blades
  IBM - virtual loaner program to QS20 Cell blades

## Slide 71: Questions ?
Samuel Williams, Leonid Oliker, Richard Vuduc, John Shalf, Katherine Yelick, James Demmel, "Optimization of Sparse Matrix-Vector Multiplication on Emerging Multicore Platforms", Supercomputing (SC), 2007.
Samuel Williams, Jonathan Carter, Leonid Oliker, John Shalf, Katherine Yelick, "Lattice Boltzmann Simulation Optimization on Leading Multicore Platforms", International Parallel & Distributed Processing Symposium (IPDPS), 2008.
Best Paper, Application Track
Kaushik Datta, Mark Murphy, Vasily Volkov, Samuel Williams, Jonathan Carter, Leonid Oliker, David Patterson, John Shalf, Katherine Yelick, “Stencil Computation Optimization and Autotuning on State-of-the-Art Multicore Architecture”, Supercomputing (SC) (to appear), 2008.