## Slide 1: SpMV (key ML kernel) inefficient on fast accelerators
Low Arithmetic-Intensity (OPS/Fetched-Byte)
Read
M
Read
Read
Time
Iteration n
Iteration n+1
Iteration n+2
CPU idle time
>99.9%
CPU busy time <0.1%
M
M

## Slide 2: Common Solution: Efficient Formats
Space-Efficient Formats
  Compressed Sparse Row (CSR)
  Variations (CSR-DU/VI)
2.5x compression ratio
Read
CSR
Read
CSR-DUVI
1.5x-4x Speedup
M
M
CSR-DU
CSR-VI

## Slide 3: New Solution: BZIP2 (Roman Kaplan)
BZIP2-compressed matrix
A bit longer to decompress
A lot shorter to read
Read
CSR
Read
CSR-DUVI
M
Read
BZIP2 + CSR-DUVI
2x-20x Speedup
M
1.5x-4x Speedup
M

## Slide 4
Chart: 
| 0.4 | 30000 | 100000
CSR_Horizontal_Roof | 695454.55 | 695454.55 | 695454.55
Achieved Performance | 21.21 | 33.28 | 32.65 | 69.14 | 93.01 | 99.35 | 195.01 | 210.3
CSR_w_BZIP_Horizontal_Roof | 55548.11 | 55548.11 | 55548.11
CSR_DU_w_BZIP_Horizontal_Roof | 65843.05 | 65843.05 | 65843.05
CSR_VI_w_BZIP_Horizontal_Roof | 43549.69 | 43549.69 | 43549.69
CSR_DUVI_w_BZIP_Horizontal_Roof | 48758.34 | 48758.34 | 48758.34
Conclusions
CSR + sBZIP2
(3.14, 93.01)
CSR-DU
(0.75, 32.65)
CSR-DU + sBZIP2
(8.71, 195.01)
CSR-VI + sBZIP2
(3.16, 99.35)
CSR-VI
(0.74, 33.28)
CSR-DUVI + sBZIP2
(8.85, 210.3)
Ridge Point with DUVI + sBZIP2 compression: 2343 Flops/Byte
Ridge Point with CSR + sBZIP2 compression: 2670 Flops/Byte
CPU Peak Perf.
Peak Perf. With sBZIP2 +
CSR-DU/+VI Overhead
External Storage BW
Main Memory BW
Compressed Input  Higher Operational Intensity